## Slide 1: PCEP Extensions for Signaling Multipath Information
M. Koldychev – Cisco Systems (mkoldych@cisco.com) – Presenter
M. Sivabalan – Cisco Systems (msiva@cisco.com)
T. Saad – Juniper (tsaad@juniper.net)
V. Beeram – Juniper (vbeeram@juniper.net)
H. Bidgoli – Nokia (Hooman.Bidgoli@Nokia.com)
B. Yadav – Ciena (byadav@ciena.com)
IETF 106 – Singapore PCE Working Group

## Slide 2: Motivation
Signaling Multiple Segment-Lists of an SR Candidate-Path
  SR policy POL1 <headend, color, endpoint>
  Candidate-path CP1 <proto, originator, discriminator>
  Weight W1, SID-List1 <SID11...SID1i>
  Weight W2, SID-List2 <SID21...SID2j>
Splitting of Requested Bandwidth
  request a path with 100 Gbit of bandwidth, but all available links in the network have only 50 Gbit capacity
Providing Backup ERO for Protection
  allow paths to protect each other in case of failure

## Slide 3: Multipaths
We include multiple ERO objects within the same PCEP LSP, rather than creating multiple PCEP LSPs and associating them. This gives the desirable property that a single PCRpt/PCUpd/PCInit carries all the forwarding information in a single shot.
We introduce a new object, ERO-ATTRIBUTES:
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Optional TLVs can encode additional attributes/state about the path, such as weight for UCMP, protection, etc.

## Slide 4: Protection
We allow EROs to protect each other in various combinations. For this purpose, we introduce the MULTIPATH-BACKUP TLV:
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ERO Path ID. |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Backup ERO Path ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
We plan to extend this TLV in the next revision to allow for more rich protection scenarios.

## Slide 5: Capability
PCC needs specify how many multipaths it is able to install in forwarding. For this, we introduce the MULTIPATH-CAP TLV:
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Number of Multipaths | Reserved |B|W|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
This TLV is mandatory in the OPEN object (if the PCC/PCE supports this draft), but can also be optionally carried in the LSP object to override the global values. For example, if a given Tunnel specifically does not want multipaths, it can set the Number of Multipaths to 1.